## Slide 1
HEC-RAS
Giulia Sofia, PhD

## Slide 2: Overview
HEC-River Analysis System is a software for river hydraulic evaluations:
  Steady flow profiles
  Unsteady flow simulations (both 1D along rivers or channels and 2D floods over plains)
  1D Sediment analysis and stable channel evaluations
  1D water quality analysis

## Slide 3: Overview
The most comprehensive and up to date reference is available under the help menu. Please refer to
  the hydraulic reference for the basic theory and to know how the hydraulic theory is applied as a numerical method
  the User Manual to understand the program structure and the meaning of the various screens

## Slide 4: Main references
HEC-RAS User's Manual. US Army Corps of Engineers
https://www.hec.usace.army.mil/confluence/rasdocs/rasum/latest
HEC-RAS Hydraulic Reference Manual 2020
https://www.hec.usace.army.mil/confluence/rasdocs/ras1dtechref/latest
HEC-RAS Documentation. US Army Corps of Engineers.
https://www.hec.usace.army.mil/confluence/rasdocs
HEC-RAS Mapper User’s Manual
https://www.hec.usace.army.mil/confluence/rasdocs/rmum/latest
HEC-RAS 2D User's Manual. US Army Corps of Engineers
https://www.hec.usace.army.mil/confluence/rasdocs/r2dum/latest

## Slide 5: Overview
Open and save the project
Open the geometry editor
Open the steady flow editor
Open the unsteady flow editor
Open the steady plan editor
Open the unsteady plan editor
Open graphical results
Open tabular results and notes
RAS Mapper

## Slide 6: Overview
A single HEC-RAS project works in a dedicated folder you set at start.
RAS saves a lot of working file. The main ones are the following:
  the project file .prj
    contains the summary of all the project
  the geometry files .gxx (.g01, .g02, etc)
    contain the geometric and topographic data (perhaps in the up to date and the design scenarios)
  the unsteady flow files .uxx
    contain the initial and boundary condition data for an unsteady flow analysis
  The plan files .pxx
    contain the information needed for a simulation, that is a geometry reference, a boundary condition reference and other simulation parameters (tolerances, settings, time steps, etc)

## Slide 7: A RAS project
RAS project
Area1 geometry (g01)
Area2 geometry (g02)
Area 3 geometry (g03)
Unsteady flows condition (u01)
TR 50y unsteady flow (u02)
2022 flood flow (u03)
Event 1 (p01)
Event 1 (p02)
Design TR 50y unsteady analysis (p03)
Area 3 unsteady analysis (p04)

## Slide 8: A RAS project
Pallavi, H., Ravikumar, A.S. (2022)
The needed information is stored in specific files within the working folder

## Slide 9: For Windows
A single HEC-RAS project works in a dedicated folder.
Terrain data [as *.HDF file]
Geometry data *.g01
Plan data *.p01
  *.p01.HDF
Results from RASMAPPER
Unsteady flow file
Mannings’ file

## Slide 10: Plan data
Plan data *.p01
It is a simple text file, that contains [amongst others]
the plan name,
The simulation window
the flow and geometry file used by the project

## Slide 11: Unsteady flow file
Unsteady flow file *.u01
It is created AFTER the input hydrographs are set in the program.
For each boundary condition, it includes
- the name,
the computational interval,
The flow hydrographs values
The beginning of the event

## Slide 12: From windows to linux
List of the files used by HEC-Ras
Extension | Description | Windows | Processed in NCM | Input for Linux
.prj | project file |  |  | 
.p01 | plan files |  |  | 
.g01 | geometry files |  |  | 
.u01 | unsteady flow files |  |  | 
.b01 | unsteady run files |  |  | 
.x01 | input file for geometry preprocessor |  |  | 
.O01 | binary output file |  |  | 
.bco | model log file |  |  | 
.c01 | output of geometry preprocessor |  |  | 
.dss | input / output files |  |  | 

## Slide 13: For Linux
Files needed from HEC-RAS GUI run
The HEC-RAS GUI will need to be run to provide a base set of the input files for the Linux compute.
Geometry based files
*.c01
*.x01
Text based files will need to have the ending carriage return character stripped to be Linux compatible (.x04 and b04).
*.g01.hdf
*.b01
*.p01.tmp.hdf
*.p01.hdf

## Slide 14: For Linux
Unsteady flow *.u01
not needed. The linux version reads the input flows from the *.p01.hdf file.
The NCM system has a series of python routines that read the CREST results, and embed them into the original HDF file at each run.

## Slide 15: For Linux
Unsteady flow *.b01
This file is created at the first run in windows, and it MUST exist for the linux version to run
Importantly, this file contains
- The calibration parameters
- the computational window for each run
The NCM system has a series of python routines that read the CREST results, and embed the beginning and end into the file
Nda: Initial restart must be set to F [False]

## Slide 16: For Linux
The NCM system has a series of python routines that read the p01.hdf file, and remove the results from any previous run.
*.p01.temp.hdf
The *.p01.tmp.hdf is derived from an HEC-RAS GUI compute that produces the file *.p01.hdf.
The computed file includes the event conditions, the plan and geometry data, and the results.
In windows, the software ‘transforms’ the p01.hdf file into a file named *.p01.tmp.hdf. This step does not exist in the linux version. Nonetheless, the software needs such file to run.
The *.p01.hdf cannot simply be renamed to *.p01.tmp.hdf

## Slide 17: Structure of each folder for NCM
Folders where flows and results are stored
List of correspondence between outlet names from CREST, and HECRAS boundary condition names
Terrain data as *.ASC file
Coordinate system of the project

## Slide 18: Questions?